## Slide 1
The Stuart City Reef Trend, South Texas
A presentation for:
Raven Forest Operating, LLC
August 4, 2021
Lowell Waite
Department of Geosciences
University of Texas at Dallas

## Slide 2
Outline
Introduction and regional geologic setting
Edwards petroleum system and depositional facies
Pioneer Natural Resources (PNR) data acquisition, core analysis, and 3D seismic facies mapping
Edwards reef reservoir characterization
Raven Forest prospect, east Texas

## Slide 3
GSA South Central Mtg, Austin, TX (2013)
AAPG ICE, Calgary, Canada (2010)
This presentation is a compilation of two talks, which together summarize key learnings from the PNR Edwards exploration project, south Texas (2004 – 2008)

## Slide 4
Stuart City Trend, south Texas
Lower Cretaceous (middle Albian) reef complex extending for > 1000 km across
11,000 – 15,000+ ft.
String of natural gas accumulations within reef facies, in combination
south and east Texas, part of a larger system that rims the circum-GOM Basin
Avg. porosity: 4 - 5%
High temps, pressure
SAT
HOU
AUS
Bottom Line:
Microporous
tight gas reservoir
Stuart
City
Reef
Trend
structural -
stratigraphic traps;

## Slide 5
Bee
Goliad
Live Oak
Karnes
McMullen
LaSalle
Atascosa
Wilson
Dewitt
Lavaca
Colorado
Fayette
50 mi / 80 km
Stuart City
Dilworth
Kawitt
Pawnee
Buchel
Yoakum
SAT
HOU
DFW
Stuart City
Reef Trend
Word
Washburn
Ranch
Moray
EDWARDS
(ALBIAN)
SHELF MARGIN
SLIGO SHELF MARGIN
(NEOCOM. – APTIAN)
Edwards reef
gas field
Stuart City Gas Fields in South Texas
1.3 TCFG from + 700 wells

## Slide 6
Cretaceous stratigraphy, south Texas
145
140
135
130
125
120
115
110
105
100
95
90
85
80
75
70
65
Maast.
Camp-
nian
Santonian
Coniacian
Turonian
Ceno-
manian
Albian
Aptian
Barrem.
Hauteriv.
Valangin.
Berrias.
Lower Cretaceous
Upper Cretaceous
Stage
Coahuilan
Comanchean
Gulfian
Trinity Division
Navarro
Taylor
Austin
Eagle
Ford
Wash-
ita
Freder-
icksburg
Upper
Mid.
Lower
Series
Group
Escond.
Olmos
San Miguel
Upson
Anacacho
Austin Chalk
Eagle Ford
T
R
Lithostratigraphy
Supersequences
Buda
Del Rio
Georgetown
Edwards
SC
Glen Rose
Bexar
Cow Ck.
James
Pine Island
Sligo Reef
Sligo
Hensel
Hosston
Cotton Valley/Bossier
2nd - order
(T-R cycles)
T
R
R
T
R
T
R
T
R
T
R
T
R
T
R
T
Zuni II Supersequence Set
(Sloss, 1988)
A
B
Reef
Shelf l.s.
Basinal l.s.
Marl / shale
Sandstone

## Slide 7
Facies
Shallow carb. platform
Deep shelf / shelf basin
Slope & basinal
Land / supratidal
Reef margin
Regional Lower Cretaceous paleogeography
East Texas
Basin
Llano Uplift
Maverick
Basin
San
Marcos
Arch
Salt Basin
Rio Grande
Stuart City/Edwards
Reef Margin
(Middle Albian)
Comanche
Platform
updip limit
of salt
Devil’s River
trend
0
50 mi
PNR study area
Raven Forest
Edwards prospect

## Slide 8
Edwards Reef:
Petroleum system and
Depositional facies

## Slide 9
Edwards / Stuart City Trend Petroleum System
Austin - Eagle Ford
Midway - Wilcox
Edwards
Buda -
Del Rio -
Georgetown
gas-filled
reservoir
Lower Cretaceous
Up. Cret.
Tertiary
Albian
Cenom.
Tur. -
San-Con
Maast.-
Camp.
L. Eoc. -
Paleoc.
Reservoir facies
Lateral and top seal facies
Low-perm lagoonal wackestones
Non-porous planktonic foram -calcisphere wackestones
Organic-rich calcareous shale, chalk
Main shelf-margin fault
Non-organic terrigenous shale, s.s.
Source rock(s)
5 km
(vert. not to scale)
Trap type: combination
Microporous rudist-algal reef boundstones, packstones, and skeletal grainstones
SE
BVW

## Slide 10
The Rudists…..Cretaceous bivalve reef builders
Lower
valve
1 in.
Upper
valve
Distinctive shell wall
(Coogan, 1978)
(Kaufmann & Sohl, 1974)
Floatstones
(muddy
matrix)

## Slide 11
The Rudists…..Cretaceous bivalve reef builders
Lower
valve
1 in.
Upper
valve
Distinctive shell wall
(Coogan, 1978)
(Kaufmann & Sohl, 1974)
Conceptual drawing of a typical rudist bank,
Tethyan seaway (from Skelton, 2003, The Cretaceous World)
(Coogan, 1978)
(Kaufmann & Sohl, 1974)
(Kaufmann and Sohl, 1974)
Intertidal
Inner
Lagoon
Middle
Lagoon
Outer
Lagoon
Center
Lagoon
0
Barrier
Back
0
Barrier
Rudist
0
Barrier
Foreslope
0
Outer
Foreslope
Caribbean Rudist Framework Assemblages
Floatstones
(muddy
matrix)

## Slide 12
zzzzz
A
A’
Southeast
Stuart City
Fredericksburg
Austin Chalk – Eagle Ford
Washita
Glen Rose
Pearsall
Hosston - Sligo
Stuart City margin at Pawnee Field, Bee Co., TX
Pawnee Fld.
25 km
15 mi
500 ft
150 m
VE=100x
Peritidal shelf carb.
Subtidal shelf carb.
Deep shelf carb.
Reefal shelf margin
Slope
Flooded shelf mudrocks
Nearshore siliciclastics
Superseq.
boundary
13
14
15
16
Depth
(x1000 ft)

## Slide 13
1
2
3
4
5
6
Basinal
Fore-reef / Slope
Reef Margin /
Reef Flat
Reef Wall
Back Reef /
Shelf Interior
1
2
3
4
5
6
Shoal
Stuart City Trend: Multiple rock types, six major environments
2
3
3
4
5
6
Reef margin at Pawnee Field, Bee Co., TX

## Slide 14
Edwards reefs: a high degree of internal heterogeneity
core/log scale: below 3-D seismic resolution
Difficult to calibrate facies to standard logs
top reef
1
6
-
3rd-order
cycles

## Slide 15
Edwards Reef:
PNR data acquisition,
core analysis, and
3D seismic facies mapping

## Slide 16
Stuart City Trend Exploration History, South Texas
Completions per Year
Initial exploration
phase
late 1970’s
boom
Pioneer Nat. Res.
expansion program
begins
initial
laterals
Pawnee
Field
infills &

## Slide 17
Stuart City Trend Exploration History, South Texas
Completions per Year
Initial exploration
phase
late 1970’s
boom
Pioneer Nat. Res.
expansion program
begins
initial
laterals
Pawnee
Field
infills &
purchased > 25,000 line-miles 2D seismic
acquired ~ 1700 mi2 (4400 km2) new 3D seismic
86 wells (deep pilots w/ horizontals)
7 new extensive cores (300 – 1000 ft)
Acreage leasing:
> 300,000 acres @ $100 -150/acre
Numerous reservoir, production data
PNR data acquisition (2005 – 2008)

## Slide 18
Simplified facies for seismic mapping
Information on ~ 60 cores, detailed description of 7 new PNR cores
reef core:
50 m
5 km
shelf margin reef
lagoonal shoal /
Sligo
margin
patch reef
rudist PS/BS
reef flank:
rudist WS
back reef:
algal-coated
island-shoal:
skeletal GS
lagoon:
miliolid WS
sea level
slope:
planktic
foram -
echinoid
WS
BS = boundstone; GS = grainstone; PS = Packstone; WS = wackestone
skeletal PS

## Slide 19
Back reef and Back-reef shoal
2 in.
Rudist packstone
(algal coated)
Skeletal grainstone
2 in.

## Slide 20
Reef flat
2 in.
2 in.
Caprinid and Toucasid floatstones

## Slide 21
Reef core / Reef wall
14, 620 ft.
14, 624 ft.
4 in.
coral
laminar
stromatop.
red
algae
rudist
frag
Litho-
codium
0.25 in.
strom.
encrusting
red
algae
stromatoporoid
strom.
strom.
0.25 in.
Rudist –
stromatoporid –
algal
boundstones

## Slide 22
Simplified facies for seismic mapping
Information on ~ 60 cores, detailed description of 7 new PNR cores
Calibration of simplified facies from core to 3D seismic allows for regional mapping
reef core:
50 m
5 km
shelf margin reef
lagoonal shoal /
Sligo
margin
patch reef
rudist PS/BS
reef flank:
rudist WS
back reef:
algal-coated
island-shoal:
skeletal GS
lagoon:
miliolid WS
sea level
slope:
planktic
foram -
echinoid
WS
BS = boundstone; GS = grainstone; PS = Packstone; WS = wackestone
skeletal PS

## Slide 23
isochron
interval
Simplified depositional facies from core calibrated to 3D seismic
Reef core
Reef flank
Back reef
Lagoon
Core - based model
cored
interval

## Slide 24
Island-shoal
complex
Lagoon
Edwards reef margin
Prominent
ridges
reef cores)
Edwards
reef margin
(isolated
reef core facies
reef platform &
backreef facies
Lagoon
Top Edwards structure
with seismic facies
interpretation drape
0.5 km
Core - based model

## Slide 25
basin
slope &
slope & basin
lagoon
Sligo shelf margin
(buried)
Detailed regional mapping
10 km / 6 mi
Bee Co.
Live Oak Co.
Karnes Co.
Dewitt Co.
Reef margin
Reef flat
Back reef
Back reef shoal
Patch reef
Struct.
low
fault
N
Shelter Rock
Speary / Kawitt
Kenedy
Pawnee
Based on 3D seismic, core, well logs
Belize, C.A.
Crooked Island, Bahamas
Great Barrier Reef,
Australia
(images from
Google Earth)
10 km / 6 mi
10 km / 6 mi
10 km / 6 mi

## Slide 26
Edwards Reef:
Reservoir Characterization

## Slide 27
Schroeder #1 well, Pawnee field (horizontal plugs)
0.001
0.01
0.1
1.0
10
100
1000
0.0
2.0
4.0
6.0
8.0
10.0
12.0
Permeability (md)
porosity (%)
Mudstone
Rudist wackstones
Rudist packstones
Coarse grainstones
Fine grainstones
Boundstones
Semi-log cross plot: Porosity – permeability by fabric
Bee Co., TX API # 42-025-33208-0000
Avg porosity < 5%
Permeability << 1millidarcy
= Tight limestone

## Slide 28
Stuart City Trend reservoir description
Rudist-bearing reef rocks and associated rock fabrics are extremely tight,
with porosity generally less than 5% and permeability less than 1 md
Major pore network consists of micropores (1 – 6 microns in size) associated
with early transformation of Mg-calcite to microrhombic calcite
Pore throat sizes are sub-micron
Micropores occur within grains, in algal-coated grain rims, and in the
ubiquitous very fine peloidal mud matrix,
in all depositional facies

## Slide 29
Plane light; blue
epoxy
Micropores in
lime matrix
Micropores in
foram shells
Blue-UV light
Mud-rich packstone
Grainstones
-- Microporous limestone reservoir

## Slide 30
Plane light; blue
epoxy
Micropores in
lime matrix
Micropores in
foram shells
Blue-UV light
Mud-rich packstone
Grainstones
-- Microporous limestone reservoir with submicron pore throats --
width of human hair: 100 microns
avg cloud water droplet: 10 microns
red blood cell diameter: 6-8 microns
Pore throat size determination for
5 samples from Schroeder #1, Bee Co.
Mercury injection – capillary pressure
(microns)

## Slide 31
Decline curve analysis, Pawnee Field, Bee Co., TX
1
0.5
0.1
0.05
0.01
0
1
2
3
4
5
6
7
8
Time, years
Average daily gas flow rate (normalized)
Upper Tier
Middle Tier
Lower Tier
- Hyperbolic declines
- Wide range of performance
1 - 2 BCF/well
10 - 20 BCF/well
3000’ laterals
3-stage acid
fracs
3 - 8 BCF/well

## Slide 32
De
Lagoon
Back
Lagoon
5.0
4.5
4.0
3.5
3.0
2.5
2.0
1.5
1.0
0.5
0
Avg. EUR per well (BCFG)
n = 24
n = 113
n = 85
Island
n = 127
shoal
Reef
n = 283
core &
flank
shoal /
patch reef
reef
Average well EUR by facies
Exploration risk

## Slide 33
San
Antonio
Corpus
Christi
Victoria
McMullen
La Salle
Live Oak
Bee
Sligo (Aptian) shelf margin
Edwards (Albian)
shelf margin
Maverick
Basin
Devils River
Trend
East Texas
Salt Basin
updip limit
of salt
Rio Grande
Embayment
Karnes
Dewitt
Lavaca
Colorado
Yoakum
Channel
1
2
3
4
5
6
San
Marcos
Arch
Edwards (Albian)
shelf margin
Sligo (Aptian)
shelf margin
Edwards margin: subregions
similar structural setting / fault styles
50 miles
Edwards gas field
Rio Grande Salt Basin – shallow
Rio Grande Salt Basin – deep
Pawnee Field
San Marcos Arch
Word Field complex
East Texas Salt Basin
equivalent reservoir depths, trap config. ,
gas columns, drilling & comp. strategies

## Slide 34
Edwards Reef:
Raven Forest prospect, East Texas

## Slide 35
Facies
Shallow carb. platform
Deep shelf / shelf basin
Slope & basinal
Land / supratidal
Reef margin
Regional Lower Cretaceous paleogeography
East Texas
Basin
Llano Uplift
Maverick
Basin
San
Marcos
Arch
Salt Basin
Rio Grande
Stuart City/Edwards
Reef Margin
(Middle Albian)
Comanche
Platform
updip limit
of salt
Devil’s River
trend
0
50 mi
PNR study area
Raven Forest
Edwards prospect

## Slide 36
Raven Forest Crossline 183, PSTM All Offsets
Amplitude Dim-Out
1963 Phillips- Central Coal & Coke A #1
Cored, logged and tested 165 net feet of gas
with porosity ranging from 5 to 13% .
Massive, steep shelf margin w/ deep lagoon
8 – 12% core porosity suggests a more conventional-type pore system; microporous mud matrix may also contribute to reservoir performance

## Slide 37
Top Edwards structure suggests multiple reef cores surrounded by reef flank facies

## Slide 38
Scale comparison
(Pawnee and Stuart City field maps
from Cook, 1979)

## Slide 39
Edwards reef trend: conclusions
Edwards reef fields in south TX are essentially tight limestone reservoirs with limited porosity; reservoir consists mostly of a microporous limestone mud matrix with sub-micron pore throats
Individual reef complexes consist of 5 basic environments (reef core/reef flank/shoal/back reef/lagoon), each of which contains multiple rock types/facies
Vertical and lateral distribution of facies is highly heterogeneous (sub-seismic scale)
Raven Forest area (Montgomery Co., east TX) appears highly prospective as an Edwards reef target; multiple reef cores surrounded by a variable width of reef flank environments is indicated on 3D; pore system my be largely conventional
Production decline profiles show classic hyperbolic shape; extremely wide-range of reservoir performance
S. TX wells targeting reef core, reef flank, and shoal environments have highest EURs/well