## Slide 1
Geology of the Permian Basin
Lowell Waite
UT Dallas Geoscience
Permian Basin Research Lab
1/24/2022
Middle & Upper Permian
Post-Permian
Permian Basin
Petroleum System

## Slide 2
Geology of the Permian Basin: ELS (Endeavor Lecture Series)
Tectonic history – Part 1 (Big Picture)
Tectonic history – Part 2 (Regional elements: ARM, CBU, MFB)
Basement
Cambrian – Lower Ord (Wilberns/Bliss Ss., Ellenburger Gp)
Tobosa Basin stratigraphy (Mid Ord. – Mississippian)
Pennsylvanian (Morrow-Atoka-Strawn-Canyon-Cisco)
Lower Permian (Wolfcamp – Spraberry)
Middle and Upper Permian / Permian Basin petroleum system
Horseshoe Atoll

## Slide 3
Permian Chronostratigraphy
Duration: 47 m.y. (298.9 – 251.9 Ma)
lower Permian = Cisuralian
middle Permian = Guadalupian
upper Permian = Lopingian
Three Global Series
GSSPs currently undefined for three lower Permian global stage bases (Kungurian, Artinskian, Sakmarian)
Global Boundary Stratotype Section and Point (GSSP)
9 Global Stages; 4 North American Stages
(Chen and Xu, 2019)
298
296
294
292
290
298.9
Asselian
Sakmarian
293.52
290.1
Cisuralian
Artinskian
283.5
Kungurian
272.95
288
286
284
282
280
265.1
Roadian
268.8
278
276
274
272
270
Wordian
Capitan-
ian
300
268
266
264
262
260
259.1
Guadalupian
Wuchiapingian
254.14
251.90
AGE
(Ma)
258
256
254
252
250
Lopin-
gian
Changhsingian
CARBONIFEROUS
GLOBAL
STAGE
SERIES
N. AMER.
STAGE
Magnetic
Wolf-
camp-
ian
Leonard-
ian
Guad-
alup-
ian
Ochoan
polarity
units
Permo-Triassic
Mixed Superchron
Klaman Reversed Superchron
Lower Permian reversed magnetic superchron; middle – late Permian mixed superchron

## Slide 4
Select Permian Global Secular Trends
Tarim I
Tarim II
Panjal Traps
Qiangtang
basalt
Tarim III
Emeishan
LIP
Siberian
Traps
Silicic Choiyoi igneous province
South China
arc magmatism
VOLCANISM
0
2
4
CARBON
ISOTOPES
Kamura
event
15
25
35
SEA TEMP (oC)
rapid
increase
decline
moderate
fluc-
ua-
ting
increase
BIO-
DIVERSITY
sudden drop
del 13C
MASS
EXTINCTIONS
end
Guada-
lupian
end
Permian
(Waite et al., 2020; data from Chen and Xu, 2019; Chen et al., 2013, Ross and Ross, 2009 )
1
2
3
4
Glacial
Intervals
1.
Siberia
2.
W. Australia
3.
Antarctica
4.
E. Australia
Permian
O2 levels:
115% of
modern
CO2:
900 ppm

## Slide 5
Middle Permian Paleogeography
(From R. Blakey)
Early Permian Paleogeography
Hot greenhouse climate: increasing aridity (increasing deposition of marine evaporites in Permian Basin
Long-term lowering of eustatic sea-level and draining of Pennsylvanian - Permian seaway

## Slide 6
Middle Permian:
Guadalupian

## Slide 7
Permian Basin Stratigraphy and Tectonic History
System
Permian
Pennsylvanian
Mississippian
Devonian
Silurian
Ordovician
Cambrian
Precambrian
Series
Ochoan
Guadalupian
Leonardian
Wolfcampian
Virgilian
Missourian
Desmoinesian
Atokan
Morrowan
Chesterian
Meramecian –
Osagean
Kinderhookian
Upper
Middle
Lower
U. Niagaran
L. Niagaran
Alexandrian
Cincinnatian
Mohawkian
Chazyan
Canadian
Ozarkian
Upper
Delaware Basin
Formations
Wolfcamp
Cisco
Canyon
Strawn
Atoka
L. Miss Lm
Woodford
Devonian (Thirtyone)
Upper Silurian (Wristen)
Fusselman
Montoya
Ellenburger
Rustler
Lamar
Cherry Canyon
Brushy Canyon
Bromide
Tulip Crk.
Mclish
Oil Creek
Simpson
McKee Sd.
Waddell Sd.
Connell Sd.
Joins
Bone
Spring
3rd Sand
Dewey Lake
Salado
Precambrian
Basement
Bell Canyon
Morrow
Barnett
Detrital
Lime
Cutoff Member /
1st Carb / Avalon
1st Sand
3rd Carb
2nd Sand
2nd Carb
Stray Sd
Castile
CBP & NW Shelf
Formations
Wolfcamp
Cisco
Canyon
Strawn
Atoka
L. Miss Lm
Woodford
Devonian (Thirtyone)
Upper Silurian (Wristen)
Fusselman
Montoya
Ellenburger
Rustler
Tansill
Queen
Seven Rivers
Grayburg
Glorieta
Goat
Seep
Capitan
Bromide
Tulip Crk.
Mclish
Oil Creek
Simpson
McKee Sd.
Waddell Sd.
Connell Sd.
Joins
U. Miss Lm
Dewey Lake
Salado
Precambrian
Basement
Yates
Morrow (NW Shelf Only)
U. Barnett
L. Barnett
Detrital
Lime
Midland Basin
Formations
Wolfcamp
Cisco
Canyon
Strawn
Atoka
L. Miss Lm
Woodford
Devonian (Thirtyone)
Upper Silurian (Wristen)
Fusselman
Montoya
Ellenburger
Rustler
Tansill
Queen
San Andres
Seven Rivers
Grayburg
Bromide
Tulip Crk.
Mclish
Oil Creek
Simpson
McKee Sd.
Waddell Sd.
Connell Sd.
Joins
Sylvan Sh.
Holt /Upper Leonard
Spraberry
Dean
Clear-
fork
U. Miss Lm
Dewey Lake
Salado
Precambrian
Basement
Yates
Wolfcamp D
Upper
Middle
Lwr
Jo Mill
Wolfcamp A
Wolfcamp B
Wolfcamp C1
Wolfcamp C2
Morrow
U. Barnett
L. Barnett
Bend Lm
Detrital
Lime
Sh & Detrital
L. SPBY Sh
Bliss
Absent
Wilberns
Bliss / Hickory / Riley
Wichita / Abo
Lower Clearfork
Yeso /
Clearfork
Tubb
Middle Clearfork
Upper Clearfork
Holt / Upr Leonard
Lwr San Andres
Lower San Andres
Upper San Andres
Delaware Mtn
Group
541
485
444
419
359
323
299
252
Ma
Early WFMP Event
Tectonic Phase
Strawn Event
Atokan Event
Morrow Event
Penn. – Early Permian
Foreland Deformation
Tobosa Basin
(Middle Ordovician to
Late Mississippian)
Moderate Subsidence
Post Orogenic Loading Rapid Subsidence;
Onset of HC Generation
Grenville Orogeny (1.3 to 1.0 bya)
Basement assembly and breakup of
Rodina supercontinent
(~ 150 million yrs. duration)
(~ 30 million yrs.
duration)
( ~ 50 million yrs. duration )
Passive Margin
Active Margin
mid – Wolfcamp unconformity
final basin fill/termination
Great American Carbonate Bank
(Late Cambrian – Early Ordovician)
TOBOSA BASIN PHASE
PERMIAN BASIN PHASE
(Reed and Waite, 2016)

## Slide 8
Culberson
Reeves
Loving
Winkler Co. TX
Ector Co. TX
Martin Co. TX
Howard Co. TX
DELAWARE BASIN
CENTRAL BASIN PLATFORM
MIDLAND BASIN
Rustler - Salado
Bone Spring
Ellenburger
Wolfcamp
Avalon
Strawn
L. Paleozoic
Atoka
Wolfcamp
Spraberry
U. Clearfork
San Andres
Seven Rivers-Queen-Grayburg
Ellenburger
Wood-
ford
Delaware Mtn. Gp.
Abo
Lower Clearfork
Tubb Ss
Upper Clearfork
Glorietta Ss
Capitan
Reef
Dean Ss
3rd Bone Spring Ss
datum: sea level
-8000
-10000
-12000
-14000
-16000
-18000
-20000
Tansill-Yates
0
-2000
+2000
-4000
-6000
Subsea
elev.
(feet)
Subsea
elev.
(feet)
0
+2000
- 2000
-4000
-6000
-8000
-10000
-12000
0
30 mi.
Permian
Penn.
Ord-Miss
West
East
The middle Permian (Guadalupian)
Central Basin Platform and Midland Basin
Shallow-water, backreef carbonates (limestones, dolomite) and evaporites
W. margin of Central Basin Platform
Massive sponge-algal barrier reef
Delaware Basin
Deep-water
basinal
sandstones
and shale

## Slide 9
(From Scholle, Goldstein, and Ulmer-Scholle, 2007)
Upper Guadalupian Depositional Facies
Lower Guadalupian Depositional Facies
Guadalupian Depositional Facies in the Pemian Basin

## Slide 10
(courtesy of Greg Wahlman)
San Andres Depositional Model

## Slide 11
Middle Permian dolomitic limestone facies of the San Andres Formation, Midland Basin, as seen in core
Cross-bedded ooid grainstones
Fusulinid packstones
Anhydrite nodules
Dolomitic siltstones (not shown)

## Slide 12
Middle Permian evaporites,
Artesia Group, Permian Basin
(Nance, 2020)

## Slide 13
Middle Permian shallow-water platform
sandstones of the Permian Basin
(Nance, 2020)

## Slide 14
Middle Permian (Guadalupian) reef trend of the Permian Basin:
Capitan Limestone
The world-famous Capitan reef, Guadalupe Mountains
El Capitan (forereef LS)
Guadalupe Peak
Capitan LS (reef)
Artesia Gp. (back-reef LS)
Delaware Mtn. Gp. (basinal sandstones)
Guadalupe Peak
elev. 8,751 ft
(2,667 m)
cross-section
(next slide)
Capitan
reef

## Slide 15
(From Scholle and Ulmer-Scholle, 2007)
Depositional Units of Middle to Late Permian exposed in the
Guadalupe Mountains of west Texas and SE New Mexico
Shelf Edge Reefs
Basin Gravity Flow
Sands & Carbonates
Shelf Evaporitic Lagoon, Tidal, and Sabkha Deposits
Cherry Canyon
Tongue

## Slide 16
(Harris, 2009)
Seismic expression of Capitan reef
Capitan reef outcrop, Western Escarpment, Guadalupe Mtns.

## Slide 17
Tubiphytes: A problematical fossil (early Carboniferous – mid Cretaceous) common in middle – late Permian and Triassic reefs

## Slide 18
(From Scholle and Ulmer-Scholle, 2007)
Depositional Units of Middle to Late Permian exposed in the
Guadalupe Mountains of west Texas and SE New Mexico
Shelf Edge Reefs
Basin Gravity Flow
Sands & Carbonates
Shelf Evaporitic Lagoon, Tidal, and Sabkha Deposits
Cherry Canyon
Tongue
Basinal
deposits

## Slide 19
(Nance, 2020)
Delaware Mtn. Group
Highly channelized, deep-water submarine fan complexes
Sands were derived from the shelf and delivered via submarine canyons (gaps in the reef?)

## Slide 20
Channels
Delaware Mountains
Deep-water channel sands in
Permian Brushy Canyon Fm,
Guadalupe Mountains, west Texas

## Slide 21
(Nance, 2020)

## Slide 22
Upper Permian:
Ochoan

## Slide 23
Late Permian Evaporites
Last phase of basin infill
Represents a regional seal for the Permian Basin petroleum system
Latest Permian: onset of oil generation

## Slide 24
Lithologies of upper Permian units of the Permian Basin
Rustler
Salado
Tansill
Yates
Seven
Rivers
Queen
Grayburg
San
Andres
Upper
Leonard
Upper
Spraberry
Rustler – Anhydrite, halite, red beds; evaporitic lagoon, sabkha
Dominantly halite, minor anhydrite, red beds;
evaporitic lagoon, sabkha
Red beds, anhydrite, halite; sabkha, evaporitic lagoon
Ss, Sltstn, anhy, dol; eolian, lagoonal, sabkha
red beds, mudstone, anhy, halite;
sabkha, evaporitic lagoonal, intertidal
ss, sltstn, carbonate mudstone, evaporites;
eolian, sabkha
Shelf to basinal carbonates (dol & ls), ss; normal marine
Shelf to basinal carbonates (dol & ls), ss, shale; normal marine
Shelf to basinal carbonates (dol & ls), organic-rich shale; normal marine
Dewey Lake
Dewey Lake – Red beds (ss & sltstn); wadi channel, eolian
Dockum
Group
basinal silt- and sandstones interbedded with organic-rich shale
Middle Permian
(Guadalupian)
Lower Permian
(Leonardian)
Upper Permian
(Ochoan)
Triassic
Artesia Group

## Slide 25
Castile varves

## Slide 26
(Kirkland, 2003)
carbonate

## Slide 27
POST-PERMIAN

## Slide 28
Permian Basin Foreland Cenozoic & Mesozoic Stratigraphic Columns & Tectonic Events
System
Series & Stages
Erathem
Cenozoic
Mesozoic
Neogene
Quaternary
Pleistocene & Holocene
Paleogene
Cretaceous
Jurassic
Triassic
Pliocene
Miocene
Oligocene
Eocene
Paleocene
Late
Early
Late
Early
MIddle
Late
E.
Middle
Scythian
Anisian
Ladinian
Carnian
Norian
Rhaetian
Hettangian
Sinemurian
Pliensbachian
Toarcian
Aalenian
Bajocian
Bathonian
Callovian
Oxfordian
Kimmeridgian
Tithonian
Berriasian
Valanginian
Hauterivian
Barremian
Aptian
Albian
Cenomanian
Turonian
Coniacian
Santonian
Campanian
Maastrichtian
Permian Basin
Formations
Cenozoic and Mesozoic Tectonic Events
Ogallala
Various Local
Intrusives and
Volcanics
Fredericksburg
Edwards
Comanche Peak
Paluxy
Dockum /
Chinle
Group
Santa Rosa
Tecovas
Regional Uplift Of Permian Basin Due To Thermal Uplift Associated With Late
Stage GOM Rifting And Initiation Of GOM Spreading
Rifting In Gulf of Mexico (GOM)
Laramide Compression – Reactivation Of
Some Late Paleozoic Faults
Basin & Range
Extension
In Westernmost
Permian Basin
Inundation By Cretaceous Seaway
Regional Uplift Of Permian Basin Due To Thermal Uplift Associated With Basin And Range Extension West Of
Permian Basin
Trujillo
Cooper Canyon
Triassic sedimentation derived from uplift south of Permian Basin associated with initial stages of Gulf of Mexico rifting
onset of major oil generation (Late Permian)
Late Cret. burial and 2nd period of major oil generation
Wichita peneplain

## Slide 29: Dockum Group subsurface waters, Midland Basin
Trinity
Tecovas
Santa
Rosa
Dewey
Lake
Rustler
Salado
Fresh Water
Brackish Water
Saline Water
Trujillo
Tecovas
(Display by Evan Kelly, Pioneer)

## Slide 30: NW – SE cross section across Midland Basin showing increasing truncation of Dockum Group to south
Upton
Glasscock
Sterling
Irion
Midland
Reagan
B
B’
Flattened on Cretaceous unconformity
NW
SE
B
B’
Cretaceous
Triassic
Permian
U Santa Rosa
M Santa Rosa
Dewey Lake
Rustler
Salado
Trinity
L Santa Rosa
Tecovas
Trujillo
Tecovas
U Santa Rosa
M Santa Rosa
L Santa Rosa
Dewey Lake
Rustler
Salado
Midland
Upton
Reagan
Irion
5
5
10
10
15
15
Water Zone
N
Dockum Group becomes progressively truncated to the south due to Late Jurassic (Late Callovian to Early Oxfordian) erosion, which was caused by thermal uplift associated with end of rifting breakup in the Gulf of Mexico
(cross-section courtesy of Evan Kelly, Pioneer)
Trujillo
Tecovas
M Santa Rosa
U Santa Rosa
L Santa Rosa
Dewey Lake
Rustler
Salado
This eroded surface, the sub-Cretaceous unconformity, is known as the Wichita peneplain

## Slide 31
Central Basin Platform
Midland Basin
Midland
Ector
Winkler
Horizontal Reference Line
Cretaceous
Dewey Lake & Triassic
Salado
Salado
Yates
Yates
West
East
Evidence of Subtle Upper Cret. – Paleogene Laramide Reactivation of Central Basin Uplift
Cretaceous, Triassic, Upper Permian evaps, and Yates are all slightly flexed and uplifted along edge of Central Basin Uplift
Flexing and uplift
of shallow strata
(WTGS 1984 Cross Section)
(Tim Reed, Pioneer)
More significant uplift occurs in Neogene (Basin and Range) that significantly impacts petroleum system along western margin of Delaware Basin

## Slide 32
Permian Basin Petroleum System

## Slide 33
Permian Basin, West Texas: A World-class Hydrocarbon Province
51 oil fields with “giant” status (>100 million barrels of oil cumulative production), including
5 fields with > 1 BBO
30 mi
Cumulative oil production ~ 36.5 billion barrels of oil + 109 trillion cubic ft. gas
Oil and gas fields colored by age of reservoir
U. Permian – San Andres
L. & U. Ordovician
Penn - Strawn
Penn – Canyon/Cisco
L. Permian - Wolfcamp
L. Permian - Leonard
U. Permian – Queen
U. Permian – Yates
M. Permian – San Andres/Grayburg
Reservoirs at every
stratigraphic interval;
numerous prolific
HC source rocks
map source: Geomap
Midland
Carlsbad
TX
NMex
Vast unconventional
reserves, primarily in
Late Penn, Wolfcampian,
and Leonardian shales
Yates
> 1.4 BBO
Slaughter
1.25 BBO
Wasson
> 2.1 BBO
Kelly-Synder
1.3 BBO
Spraberry Trend
1.1 BBO

## Slide 34
*
*
*
*
*
*
*
HC source rock interval
*
regional
seal
Permian Basin Conventional Reservoirs and Source Rock Intervals
Evaporites
Dolomite
Limestone
Sandstone/siltstone
Shale
Main Lithologies
(modified from BEG, 1983, Atlas of Major Texas Oil Reservoirs,
and Dutton et al., 2005)
(size of green bubbles are proportional to total conventional reserves)
Barnett
Middle Permian: 54%
Lower Permian: 20%

## Slide 35
Conventional hydrocarbon play types of the Permian Basin
(Dutton et al., 2005, AAPG Bulletin, v. 80, p. 553-576)
(n = 13)
(n = 4)
(n = 2)
(n = 7)
(n = 1)
(n = 2)
(n = 2)
(n = 3)
34 total conventional play types recognized and mapped by Texas BEG
These plays are fully documented in 2004 DOE report

## Slide 36
(Potter et al., 2020)
Conventional petroleum systems
Permian Basin Crude Oil Production
Millions of Barrels per Day
Unconventional petroleum systems
“peak oil”

## Slide 37
Permian Basin Unconventional Shale Plays
(shaleexperts.com)
Note overlapping areas of multiple shale plays in both Midland and Delaware basins
Thermal maturity, reservoir pressure, small increases in perm matter!

## Slide 38
Timing: Burial History (Midland Basin center 1D model)
600
500
Proterozoic
Camb.
Ord.
400
Sil.
Devonian
Carb.
Permian
300
200
Triassic
Jurassic
100
Cretaceous
0
P
Eoc.
O
Mi.
0
-2
+2
-4
-6
-8
-10
-12
-14
Cretaceous
Triassic
Upper Permian
San Andres
Clearfork
Spraberry
Wolfcamp Shale
L. Ord (Ellenburger)
L. Ord (Ellenburger)
Woodford
Atoka
Atoka
Woodford
Tobosa Basin phase (passive margin)
Avg. subsidence = 3.2m / m.y.
1
2
3
1
Penn. - E. Perm. (Wolfc.) deformation phase
Avg. subsidence = 17.1m / m.y.
2
Pangean uplift /
emergence
E. to M. Perm. (Leon.-Guad.) loading phase
Avg. subsidence = 116 m / m.y.
3
Late K
burial
Late Permian: Onset of
major oil
generation
Max. burial;
2nd oil gen.
pulse
Laramide,
Basin & Range
uplift
depth
(x1000 ft)
Age (Ma)
Structural traps
Late Tertiary
uplift

## Slide 39
Empirical studies of uplifted areas worldwide have shown that uplift of previously trapped oil and gas
accumulations results in dissipation and loss of those hydrocarbons. With only
1500 m (~4900 ft) of uplift, most hydrocarbons can be lost from a trap, depending on seal strength.
Impact of uplift:
  Hydrocarbon generation shuts down in kitchens.
  Uplift may distort original trap and induce remigration.
  Uplift results in erosion, diminishing overburden pressure. With less
  overburden pressure, the original reservoir pressure can exceed the strength
  of the seal, causing it to fracture and hydrocarbons escape (blown seal)
  If seal integrity is largely maintained, then less overburden pressure can
  reduce reservoir pressure below bubble point, causing gas to come out of
  solution and cause gas cap expansion in the reservoir, which forces liquid
  hydrocarbons beyond the spill point. This can result in gas-only
  accumulations or highly variable GOR’s across an area
  For uplifted source rocks, low permeability may allow them to retain
  hydrocarbons, but subject to pressure reduction and solution gas expansion, resulting in
  low or erratic pressure and variable GOR’s
Impact of Tectonic Uplift on Hydrocarbon Accumulations
(list from Tim Reed, Pioneer)

## Slide 40
WTGS Regional Cross Section Across Delaware Basin & Diablo Uplift Showing Post-Permian Uplift
Basin and Range
Down-faulting
Basin and Range
Down-faulting
CBP and Midland Basin uplifted < 3000 ft.
Western side of Delaware Basin uplifted > 4900 ft.

## Slide 41
2.45 km
0.65 km
1.8 km
(5,900 ft)
of
uplift
(modified from Barker and Pawlewicz, 1987)
Burial history curve, western margin of Delaware Basin

## Slide 42
Oil and gas fields
First discovery was at Westbrook Field, Mitchell Co, TX (1921)
5 individual fields with >1 BBO cumulative production
51 oil fields with “giant” status (>100MM BO cumulative prod.)
Prolific conventional hydrocarbon basin:
30 mi
colored by age of reservoir
L. & U. Ordovician
Penn - Strawn
Penn – Canyon/Cisco
L. Permian - Wolfcamp
M. Permian - Leonard
U. Permian – San Andres
U. Permian – Queen
U. Permian – Yates
Slaughter
Kelly-Snyder
Yates
Spraberry
Trend
Wasson
New unconventional reserves will likely eclipse historical conventional production
Midland
Cumulative oil production (through yr. 2000) =
29 BBO (+ 75 TCFG)

## Slide 43
30 mi
Consequences of too much tectonic uplift on a major petroleum basin
(Midland Map Co.)
> 1500 m uplift

## Slide 44
Lithology
System
Permian
Pennsylvanian
Mississippian
Devonian
Silurian
Ordovician
Cambrian
Precambrian
Series
Ochoan
Guadalupian
Leonardian
Wolfcampian
Virgilian
Missourian
Desmoinesian
Atokan
Morrowan
Chesterian
Meramecian –
Osagean
Kinderhookian
Upper
Middle
Lower
U. Niagaran
L. Niagaran
Alexandrian
Cincinnatian
Mohawkian
Chazyan
Canadian
Ozarkian
Upper
Midland Basin
Formations
Wolfcamp
Cisco
Canyon
Strawn
Atoka
L. Miss Lm
Woodford
Devonian (Thirtyone)
Upper Silurian (Wristen)
Fusselman
Montoya
Ellenburger
Rustler
Tansill
Queen
San Andres
Seven Rivers
Grayburg
Word
Whitehorse
Bromide
Tulip Crk.
Mclish
Oil Creek
Simpson
McKee Sd.
Waddell Sd.
Connell Sd.
Joins
Sylvan Sh.
Holt / Upper Leonard
Spraberry
Dean
Clear-
fork
U. Miss Lm
Dewey Lake
Salado
Precambrian
Basement
Yates
Wolfcamp D
Upper
Mid
Lower
Jo Mill
Wolfcamp A
Wolfcamp B
Wolfcamp C1
Wolfcamp C2
Morrow
U. Barnett
L. Barnett
Bend Lm
Detrital
Lime
Sh & Detrital
Bliss / Hickory / Riley
Wilberns
Reserves from unconventional resource plays rival those of conventional reservoirs
L. Miss carbonates (minor)
Devonian carbonates
Silurian carb.
L. Ord (Ellenburger)
= Major hydrocarbon reservoir interval
Hydrocarbon Source Rock Interval
Simpson
Woodford
Barnett
Atoka
Penn.
Wolfcamp
L. Sprab./
Bone Spring
San Andres
Yates-Grayburg
Wolfcamp carbonates and shale
Dean-Spraberry /Bone Spring
Penn. carbonates and clastics
Permian Basin petroleum system: Summary
Numerous world-class hydrocarbon source rocks
Porous and permeable reservoirs at virtually every stratigraphic level
Numerous traps (structural and stratigraphic)
U. Perm evaps.
(Regional seal)
Upper Permian evaporites constitute a highly efficient regional seal
Preservation issue in western portion of Delaware Basin due to > 1500 m of tectonic uplift

## Slide 45
Permian Basin Research Lab at UT Dallas
Dr. Robert J. Stern and Mr. Lowell Waite, Co-Directors
Goals:
Advance understanding of all geologic aspects of the Permian Basin through open applied research,
linking academia and industry
Educate and better prepare students for professional careers in the oil and gas industry
-- established January 2019 --
Graduate courses offered:
https://labs.utdallas.edu/permianbasinresearch/
Geology of the Permian Basin
Petroleum Geoscience
Paleo Earth Systems: Global Themes
Carbonate Sedimentology
Thank you to Endeavor for this opportunity!