## Slide 1
Re-exploring the Eastern Shelf of the Midland Basin
Lowell Waite
Department of Geosciences
Permian Basin Research Lab
University of Texas at Dallas
Permian Basin Section - SEPM
May 16, 2023

## Slide 2
The Eastern Shelf Region: Introduction
Over a century of exploration has proven the Eastern Shelf of the Midland Basin to be a prolific conventional hydrocarbon-producing region
Main reservoirs include Lower Ordovician Ellenburger dolomite and a number of middle Pennsylvanian to early Permian sandstones and limestones at relatively shallow drill depths (~ 4000 – 8000 ft MD)
The stratigraphic complexity of the region, coupled with large number of producing zones and the inherent incomplete state of the historical well data base, provides opportunities for future exploration (both conventional and semi-unconventional reservoirs)
Lower-perm, “tight” sandstones / limestones
Note: “semi-conventional” reservoirs include:
Thermally immature / marginally-mature shales

## Slide 3
Greater Permian Basin of west TX and SE New Mexico: Paleogeographic elements
100 mi.
(Engle et al., 2016)
A
A’
Eastern Shelf one of several high-standing Permo-Pennsylvanian shelves surrounding deeper Delaware and Midland basins
Eastern Shelf dips westward ~ 1.3 degrees
General stratigraphy: thin Pre-Penn (mostly L. Ord. Ellenburger dolomite and U. Camb. Ss) unconformably overlain by thick Pennsylvanian to lower Permian carbonate and clastic units (~ 4000 – 8000 ft. MD)
Note location of Ft. Chadbourne fault system: chain of small basement-involved structural blocks;
upthrown to east
Uplift
A
A’
Ft.
Ft. Chadbourne

## Slide 4
Late Penn. (Missourian)
Pennsylvanian – Early Permian Themes
SW Laurentian region during assembly of Pangea; active margin phase: Hercynian orogeny & rise of Ancestral Rockies (Tobosa Basin becomes Permian Basin)
  Climate: Icehouse phase throughout Penn. – Early Permian, transitioning to greenhouse; Permian Basin in low-latitudes (tropics); humid w/ monsoonal precipitation
  Sea level: long-term rise and expansion of Penn. seaway; short-term: Penn cyclothems (high frequency, high amplitude glacioeustatic cycles)
  Dominance of phylloid algae as main reef builders (aragonite skeletons; limestones susceptible to early leaching )
Early Penn. (Atokan)
LAURENTIA
LAURENTIA
Gondwana
(Murphy et al., 2009)
Permian Basin
Hercynian
orogen
Laurentia

## Slide 5
Prior to middle Strawn time (pre-Odom; thick dashed line), the Eastern Shelf was a shallow-water carbonate platform (Concho Platform) constituting the eastward dipping, western margin of the actively subsiding Ft. Worth Basin
Eastern Shelf Depositional Systems
(modified from Alton Brown, 2021, after Frank Brown, BEG, 1973)
Following the rapid filling of the Ft. Worth Basin by Early Penn. Atoka and early Strawn clastics, deposition shifted to westward-dipping sedimentary systems defining the Eastern Shelf of the subsiding Midland Basin
Penn – L. Perm sediments represent a thick assemblage of numerous alternating cyclothem deposits (lowstand clastics, highstand carbonates)
NOLAN CO.
STEPHENS CO.
DALLAS CO.
Pre-Penn. – early Strawn
Concho Platform
Mid Strawn – L. Permian
Eastern Shelf
50 miles
west
east

## Slide 6
(modified from Alton Brown, 2021, after Frank Brown, BEG, 1973)
NOLAN CO.
STEPHENS CO.
DALLAS CO.
Pre-Penn. – early Strawn
Concho Platform
Mid Strawn – L. Permian
Eastern Shelf
50 miles
Paleogeography/
Eustasy
General Stratigraphy of the Eastern Shelf
west
east
Prior to middle Strawn time (pre-Odom; thick dashed line), the Eastern Shelf was a shallow-water carbonate platform (Concho Platform) constituting the eastward dipping, western margin of the actively subsiding Ft. Worth Basin
Following the rapid filling of the Ft. Worth Basin by Early Penn. Atoka and early Strawn clastics, deposition shifted to westward-dipping sedimentary systems defining the Eastern Shelf of the subsiding Midland Basin
Penn – L. Perm sediments represent a thick assemblage of numerous alternating cyclothem deposits (lowstand clastics, highstand carbonates)

## Slide 7
Late Desmoinesian - Missourian (Upper Strawn - Canyon) Paleogeography
Nolan Co.
MUENSTER UPLIFT
Pennsylvanian Eustasy
Morrow
Morrowan
Atoka
Atokan
Demoinesian
Strawn
Missourian
Canyon
Cisco
Bursam
Virgilian
Regional Stage
Group
0m
+100
Sea Level
rise
During glacial minima (highstands), massive shallow-water carbonate deposition occurs along outboard shelf margins, including a series of large, isolated carbonate mounds/reefs
During glacial maxima (S.L. lowstands), tectonically-active Ancestral Rockies uplifts and Ouachita Fold Belt shed voluminous amounts of clastics (channel/delta/slope systems) across Eastern Shelf
Short-term sea-level (glacioeustacy)
Prolonged transgression drowns the underlying L. Strawn Concho Platform; organic-rich black shales (Wolfcamp D / Cline) deposited in rapidly subsiding “starved” basins
Long-term sea-level (tectonic control)
short-
term
long-
term
(after Wright, 2020)

## Slide 8
(modified from Alton Brown, 2021, after Frank Brown, BEG, 1973)
NOLAN CO.
STEPHENS CO.
DALLAS CO.
Pre-Penn. – early Strawn
Concho Platform
Mid Strawn – L. Permian
Eastern Shelf
50 miles
Large-scale Sequence Architecture
west
east
Prior to middle Strawn time (pre-Odom; thick dashed line), the Eastern Shelf was a shallow-water carbonate platform (Concho Platform) constituting the eastward dipping, western margin of the actively subsiding Ft. Worth Basin
Following the rapid filling of the Ft. Worth Basin by Early Penn. Atoka and early Strawn clastics, deposition shifted to westward-dipping sedimentary systems defining the Eastern Shelf of the subsiding Midland Basin
Penn – L. Perm sediments represent a thick assemblage of numerous alternating cyclothem deposits (lowstand clastics, highstand carbonates)
Eastern Shelf Depositional Systems

## Slide 9
100 m
50 km
Shelf Limestone
Reef
Shale
Approximate scale
(L Waite, 1988, unpublished)
reef
complex
Large, isolated
West
Organic-rich shale
Regional
organic-rich
source (Cline)
Interregional unconformity
Interregional unconformity
Canyon –
Strawn
Cisco Group
(Lower Wolfcamp)
Regressive
phase
Transgressive
phase
Sandstone
Dolomite
max. transgressive interval
Slope & basinal Limestone
Schematic stratigraphic architecture, Penn. – lower Permian, Eastern Shelf
Landward
East
.
.
.
.
.
.
.
.
.
.
.
.
.
.
2nd- order sequence
~ 12 million yr. duration

## Slide 10
Permian
Penn.
L. Ord.
(Ellen-
burger)
Age of
reservoir
30 miles
Goal of study: better understanding of producing trends along western margin of Eastern Shelf
(Midland Map Co.)
Question: what is remaining potential ?
(via field growth, exploration, horizontal drilling, etc.)
HORSESHOE
ATOLL
EASTERN SHELF
10 miles
Starting point: Nolan County
Centrally-located; previously worked (late 1980s)
Two small Caddo core samples provided by UTD alum Jerry Bergthold
Nolan

## Slide 11
Analysis of Nolan Co. producing trends: Method
Export Nolan County wells from Enverus database including producing zone (n = 5123)
Note: Individual checking of perf zone(s) in all wells is a very time-consuming, but critical step in the identification and assignment of correct, high-resolution producing zones
Identify & map a number of high-resolution producing zones (11 total; color-coded by zone)
Analyze drilling and producing statistics (not discussed here)
3.8 % of wells in eliminated mainly due to non-reported perfs
Utilizing Petra, check perforated zones for each well; amend Enverus producing zones (nammended = 4926)
Some wells eliminated due to missing API#

## Slide 12
NW Nolan Co. type log
U. Cambrian Ss
Cisco (L. Wfmp)
Limestone
Cisco (L. Wfmp)
Sandstone
“Canyon” (L. Wfmp)
Sandstone
Penn. Reef
Strawn Sandstone
U. Strawn Limestone
Odom Limestone
Caddo Limestone
Mississippian Ls
Ellenburger (L. Ord.)
U. Cambrian Ss
GR
Resis.
GR
Resis.
0
200 ft.
showing strat. position of high-resolution producing zones (11)
GR
Resis.
Formations
Eastern Shelf

## Slide 13
NOLAN COUNTY
MITCHELL COUNTY
A wide variety of structural and stratigraphic traps…
Ft. Chadbourne
fault
Saddle Creek shelf
Crystal Falls
(modified from Brown et al, 1990)
Cisco (L. Wfmp)
Limestone
Cisco (L. Wfmp)
Sandstone
“Canyon”
Sandstone
Strawn
Ss
Penn Reef
Cambrian
Ss
Odom
Ls
Caddo
Ls
Ellenburger
Mississippian
Top Lower Strawn (Caddo)
Top Ellenburger
Top Wolfcamp
shelf
Top Penn.
Ivan shelf
(not shown)
Regional W-E detail cross-section showing Penn. – lower Perm stratigraphic architecture across western margin of Eastern Shelf

## Slide 14
NOLAN COUNTY PRODUCING TRENDS MAP

## Slide 15
1
1
1
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
Nolan County
Producing Trends

## Slide 16
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
2
2
Odom low-relief, mid-shelf carbonate buildups inboard of shelf margin; also, Caddo grainstones
L. Strawn
shelf margin
(Waite, 1991)
Nolan County
Producing Trends

## Slide 17
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
2
Odom low-relief, mid-shelf carbonate buildups, inboard of shelf margin; also, Caddo grainstones
L. Strawn
shelf margin
(Waite, 1991)
3
3
Ellenburger trend (karsted cave systems?); also, large Cisco (Cook) Ss delta system inboard of Saddle Creek shelf margin
3
Saddle Creek
shelf margin
(Heintz et al., 2017)
Nolan County
Producing Trends

## Slide 18
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
5
Canyon Ss (L. Wolfcamp) distal slope system
5
2
L. Strawn
shelf margin
(Waite, 1991)
4
Canyon Ss (L. Wolfcamp) channel, delta, and proximal slope systems (Crystal Falls shelf margin)
4
4
Crystal Falls
shelf margin
(Heintz et al., 2017)
3
Ellenburger trend (karsted cave systems?); also, large Cisco (Cook) Ss delta system inboard of Saddle Creek shelf margin
Nolan County
Producing Trends
Odom low-relief, mid-shelf carbonate buildups, inboard of shelf margin; also, Caddo grainstones

## Slide 19
(from Brown et al., 1990)
CISCO GROUP - CRYSTAL FALLS
(“Canyon Sand)
DEPOSITONAL SYSTEM
Lake Trammel,
Lake Trammel S.
fields

## Slide 21
(Ambrose et al., 2022)
Correlations: low-angle clinoform interpretation

## Slide 22
(Ambrose et al., 2022)
Tidally-influenced slope channel systems

## Slide 23
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
5
Canyon Ss (L. Wolfcamp) distal slope system
6
6
Small pinnacle reefs on L. Canyon drowned platform; large isolated reefs on L. Strawn drowned platform (bank margins from Waite, 1991)
6
6
ANSON (U. CANYON) BANK
L. Canyon –
U. Strawn
shelf margin
2
L. Strawn
shelf margin
(Waite, 1991)
4
Canyon Ss (L. Wolfcamp) channel, delta, and proximal slope systems (Crystal Falls shelf margin)
3
3
Ellenburger trend (karsted cave systems?); also, large Cisco (Cook) Ss delta system inboard of Saddle Creek shelf margin
Nolan County
Producing Trends
Odom low-relief, mid-shelf carbonate buildups, inboard of shelf margin; also, Caddo grainstones
Drowned
L. Canyon/U Strn
Platform
(w/ small pinnacles)
Drowned
Middle Strawn Platform
(w/ large isolated reef mounds)
Midland
Basin
ANSON BANK

## Slide 24
Dickens
King
Salt
Creek
Kent
Boomerang
Claremont
Cogdell
Scurry
Stonewall
Kelly
Snyder
Double
Mtn.
Fisher
Round Top
Claytonville
Ocho
Juan
Eskota
Mitchell
Nolan
Rowan & Hope
Esteban
Nena Lucia
Sterling
Coke
Jameson
Millican
I.A.B.
Higgins
Ranch
Tom Green
Irion
Schleicher
H.J.
Hulldale
Page
Pennsylvanian Reef Trend
(from Counselman, 1960)
15 mi.
Horseshoe
Atoll
Empire State Bldg.
one mile
Claytonville Reef, Fisher County
Some buildups terminate in Strawn; others, like Claytonville, continue into Canyon - Cisco
Important conventional oil reservoirs Claytonville: ~ 67 MMBO
Kelly Snyder: 1300 MMBO
Massive carbonate buildups (algal reef complexes)
500 ft.
Perforated
interval

## Slide 25
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
5
Canyon Ss (L. Wolfcamp) distal slope system
6
7
Recent horizontal wells along far eastern edge of starved Midland Basin
7
2
L. Strawn
shelf margin
(Waite, 1991)
4
Canyon Ss (L. Wolfcamp) channel, delta, and proximal slope systems (Crystal Falls shelf margin)
3
Ellenburger trend (karsted cave systems?); also, large Cisco (Cook) Ss delta system inboard of Saddle Creek shelf margin
Nolan County
Producing Trends
Drowned
Midland
Basin
Small pinnacle reefs on L. Canyon drowned platform; large isolated reefs on L. Strawn drowned platform (bank margins from Waite, 1991)
Odom low-relief, mid-shelf carbonate buildups, inboard of shelf margin; also, Caddo grainstones

## Slide 26
1
1
1
1
Ft. Chadbourne structural and combination traps; multiple zones (Cambrian Ss, Elbg., Caddo Ls, Strawn Ss., U. Strawn Ls, Penn Reef. Canyon Ss) (faults from Ewing, Tectonic Map of TX)
5
Canyon Ss (L. Wolfcamp) distal slope system
5
7
Recent horizontal wells along far eastern edge of starved Midland Basin
7
6
6
6
6
ANSON (U. CANYON) BANK
L. Canyon –
U. Strawn
shelf margin
2
2
L. Strawn
shelf margin
(Waite, 1991)
4
Canyon Ss (L. Wolfcamp) channel, delta, and proximal slope systems (Crystal Falls shelf margin)
4
4
Crystal Falls
shelf margin
(Heintz et al., 2017)
3
3
Ellenburger trend (karsted cave systems?); also, large Cisco (Cook) Ss delta system inboard of Saddle Creek shelf margin
3
Saddle Creek
shelf margin
(Heintz et al., 2017)
Nolan County
Producing Trends
Small pinnacle reefs on L. Canyon drowned platform; large isolated reefs on L. Strawn drowned platform (bank margins from Waite, 1991)
Odom low-relief, mid-shelf carbonate buildups, inboard of shelf margin; also, Caddo grainstones

## Slide 27
30 miles
Goal of study: better understanding of producing trends along western margin of Eastern Shelf (Nolan County)
(Midland Map Co.)

## Slide 28
Current work
Fisher Co.
Scurry Co. (eastern half)
Kent Co. (eastern half)
Stonewall Co.
Coke Co.
NOLAN CO.
Producing zones identification for:

## Slide 29
Fisher Co.
production
Initial impressions:
Fewer producing wells compared to Nolan Co.
More dry holes in-between existing fields; but less deep well control
Reduced Ft. Chadbourne faulting
Fewer Penn reefs (but larger complexes)
Large Canyon Ss fields; more Strawn sandstone production
Areally-large Canyon Ss, Wolfcamp Ss & Ls fields
Fewer Ellenburger fields

## Slide 30
Wells that
penetrate the
Ellenburger

## Slide 31
Re-exploring the Eastern Shelf of the Midland Basin
Summary
The Eastern Shelf is a complex geologic region with multiple producing horizons
Vertical infill drilling of existing conventional zones
Relatively low cost of drilling and completing should continue to provide favorable economics for smaller independents
Stratigraphic complexity, coupled with poorly-constrained data reporting, provide opportunity for further exploration
Application of horizontal drilling & completion technologies to tight sands and limestones
Future work
“Next-level” analysis of producing fields and trends (e.g., recent BEG report)
Application of machine learning / data mining techniques
Documentation of source rocks and migration pathways

## Slide 32
Permian Basin Research Lab at UT Dallas
Dr. Robert J. Stern and Mr. Lowell Waite, Co-Directors
Goals:
Advance understanding of all geologic aspects of the Permian Basin through open applied research,
linking academia and local industry (sharing info benefits all)
Educate and provide skills to students interested in careers in industry (experience w/ subsurface data sets)
-- established January 2019 --
https://labs.utdallas.edu/permianbasinresearch/
WEBSITE:
search “Permian Basin Research Lab”
(access to publications, presentations, key illustrations)
Email: Lowell.waite@utdallas.edu